## Slide 1
THz Photonic Device Design
by Machine Learning
Jonggeon Lee
Nano-Bio THz Photonics
Department of Electrical Engineering
POSTECH, Korea
2019. 12

## Slide 2
Introduction
Additive Reinforcement Learning
Artificial Neural Network
Distributed Bragg Reflector
1x2 Power Splitter
Summary
Contents
1
2
3
4
5
6

## Slide 3
Introduction

## Slide 4
What’s the THz wave

## Slide 5
Beyond 5G
Edholm’s law: Required date rates double every 18 months
Frequencies from 100 GHz to 3 THz are promising bands for the next generation
=> Need THz band communication

## Slide 6
THz Communication
THz has big water absorption -> optical fiber communication first

## Slide 7
Design Structure
THz optical fiber communication device
DBR Reflector
1x2 Power Splitter
Design Structure

## Slide 8
Design Method
Self-Imaging: leads to compact expressions for the positions, amplitudes, and phases of the images, is given for the first time.
Direct Binary Search (DBS)
Sweep parameter based on specific structure
Ye Tian et al., IEEE Photonics Journal, vol. 10, no. 3, June 2018.

## Slide 9
Design Method
Photonic Integrated Circuits (PICs) based on Silicon-on-Insulator (SOI)에 대한 관심 증폭

## Slide 10
What’s the Machine Learning
Machine Learning:
A computer program is said to learn from experience E with respect to some class of tasks T and performance measure P.
Deep Learning:
Deep learning is a particular kind of machine learning that achieves great power and flexibility by learning to represent the world as nested hierarchy of concepts, with each concept defined in relation to simpler concepts, and more abstract representations computed in terms of less abstract ones

## Slide 11
What’s the Machine Learning
Cat or Dog
Give Features (Ex. Ears, face shape, hair)
depends on breeds
Complicate to implement

## Slide 12
What’s the Deep Learning
Cat or Dog
Cat
Cat
Dog
Dog
Dog
???
Cat!!
Give labeled data → Find features itself

## Slide 13
Additive Reinforcement Learning

## Slide 14
Additive Reinforcement Learning (ARL)
Additive + Reinforcement
Perceptron: binary classifier
< perceptron >
A sequence of training examples , ,
where all ,
For each training example :
Predict
If : update

## Slide 15
Additive Reinforcement Learning (ARL)
Additive + Reinforcement
Reinforcement: machine learning concerned with how software agents ought to take actions in an environment so as to maximize some notion of cumulative reward.

## Slide 16
Additive Reinforcement Learning (ARL) Flowchart

## Slide 17
1 for etched (air)
0 for not etched (Si)
Binary matrix
Calculated reward
from transmission
Accumulate the reward in a summation matrix M
Normalizing summation matrix M’
Activation function
Training Phase
Inference Phase
ARL Detail Description
< Activation function >

## Slide 18
Artificial Neural Network

## Slide 19
Artificial Neural Network (ANN)
Input layer
Output layer
node
layer
hidden layer
Learning: adjust of nodes variable

## Slide 20
x
1
2
3
x
w
wx+b
y
weight
Activation
function
bias
b
x | y
1 | 2
2 | 3
3 | 4
y
2
3
4
:
Training Data
Gradient
ANN Learning Process #1
Minimize by
gradient descent algorithm

## Slide 21
b = 1
w = 1
x
4
y
5
ANN Learning Process #2
x
1
2
3
x
w
wx+b
y
weight
Activation
function
bias
b
x | y
1 | 2
2 | 3
3 | 4
y
2
3
4
:
Training Data
x
1
wx+b
y
weight
Activation
function
bias
1
by Gradient descent method

## Slide 22
T
T
Forward Design
Inverse Design
Inverse Design

## Slide 23
minimize
Cost
function
Gradient
A. Y. Piggott et al., Nature Photonics, vol. 9, no. 6, pp. 374–377, Nov. 2015.
Normal Inverse Design
FDTD is too complex and heavy to calculate gradient
: structure
: analysis method (FDTD)
: spectrum
: reward

## Slide 24
Neural
Network
Learning
Inverse Design with ANN
FDTD → Artificial Neural Network
: structure
: analysis method (ANN)
: spectrum
: reward
Artificial Neural Network
(ANN)
structures
spectrums

## Slide 25
Distributed Bragg Reflector

## Slide 26
Transfer Matrix in Multilayered Medium
From boundary condition( and are continuous)
Backward-propagation matrix
Where

## Slide 27
Distributed Bragg Reflector (DBR)
Multilayer structure of pairs of alternating materials with two different refractive index
For resonance, DBR has quarter wave optical thickness at certain design wavelength
Transfer Matrix for N+1/2 pairs DBR
Reflectance at design wavelength
Increasing N (# of pairs) & nl/nh (refractive index ratio), R converges to 1

## Slide 28
Design Platform - Structure
Start with index unknown material
@ 1 THz
@ 1 THz
DBR
,
Design wavelength: 300 um (1 THz)
Wavelength: 150 – 3000 um (5 um step)

## Slide 29
Design Platform - Algorithm
ARL
ANN
Input layer: 80 node
Output layer: 570 node
Hidden layer: 3 layer, 200 node

## Slide 30
Reflectance of DBR

## Slide 31
Spatial Distribution of E-field

## Slide 32
1x2 Power Splitter

## Slide 33
1x2 Power Splitter
Equally divide the power into the output ports

## Slide 34
Design Platform
Photonic Integrated Circuits (PICs) based on Silicon-on-Insulator (SOI)에 대한 관심 증폭

## Slide 35
E
1x2 splitter TM
R ~0.05
Power uniformity = 0.71 dB
# of data: 40,000
reward = min(T)
T
T ~0.43
R
T
Transmission
Design Platform

## Slide 36
Summary